## Slide 1: Heating and Stirring Module Design Review #5

## Slide 2: Heating & Stirring PCB
Finished routing 4-layer board
Mainly SMD components, to be assembled by hand
Designed around NUCLEO-G431KB Development board
$7 order, 5 board MOQ.

## Slide 3: Heating & Stirring PCB
Slides directly over motor housing.
Motor housing requires alteration to account for connector placement.
Solder pads for motor connection limits repairability, lowers cost.
Ventilation?
EMI Concerns

## Slide 4: Control Hub PCB
Based on NUCLEO-C071RB development board.
~25A max draw, multi-plane power bus.
Limited power output, ~100W/module fully loaded.
Fused main and module lines, emergency stop

## Slide 5: Control Hub PCB
Mounting plate, M3 screws + standoffs.
Terminal-style main connection.
MCU is over-spec, could be downsized to reduce footprint.

## Slide 6: CAN-Bus vs I2C
H&S modules will be extremely noisy.
I2C is noise sensitive, resulting in packet loss.
CAN-Bus is noise resistant by nature.
  Requires extra IC.
  Reduces connector positions.
  Modules can be “chained” together.
  Slightly slower transmission speeds, negligible in our case.
CAN-BUS Timing Diagram
I2C Timing Diagram

## Slide 7: Next Steps
Implement CAN-Bus.
  CAN Transceivers
  Hot-swappable terminating resistors
Alter housing to account for PCB changes.
  Ventilation
  Connector sizing
  Button/Screen placement
Verify high-current design with experienced peers.